|  | THABONG HOMESTEAD Proposed establishment of a new extension in Homestead, Thabong. |  |
| --- | --- | --- |

| PREPARED BY: PHETHOGO CONSULTING PO Box 43284 Heuwelsig Bloemfontein 9332 CONTACT PERSON: Mr P de Bie Tel: (051) 448 5506/7/8 Fax: (051) 448 6728 Cell: 082 415 6069 | PREPARED FOR: MATJHABENG MUNICIPALITY PO Box 708 WELKOM 9460 CONTACT PERSON: Mr F Nieuwoudt Tel: 057 916 4187 Fax: 057 916 |
| --- | --- |

# THABONG, HOMESTEAD:

PROPOSED New extension IN THABONG, HOMESTEAD of 741 erven AND STREETS situated ON A PORTION OF THE Remainder OF the farm HOMESTEAD NO 668

- appointment

The Department of Human Settlements advertised tenders in March 2011 and appointed Phethogo Consulting on 16 July 2012 to do the planning and surveying of 800 erven in Homestead based on the Matjhabeng Municipality business plan. This application is for 741 erven in Homestead, Thabong.

- BACKGROUND

The Municipality of Matjhabeng was in need of residential erven in Thabong, Homestead to be able to satisfy the waiting list for erven. According to the SDF and business plan for 2007 to 2010 there was a need of 1800 erven in Thabong. This proposed layout is situated within the present and future residential areas on the attached SDF Map and therefore in line with the SDF for this area.

In order to get the urgently needed erven, the Municipality submitted their business plan to the Department who allocated funding for the 2012/2013 to the 2014/2015 financial years. The Department appointed Phethogo Consulting by letter dated 16 July 2012 to proceed with the planning and surveying of 800 erven in Homestead, Thabong. As is indicated in the Spatial Development Framework of Thabong and Homestead, the identified portions of land have been earmarked for future extension and this area can also be serviced from the adjacent networks.

The portion of land is in the ownership of the Matjhabeng Municipality. Copy of Deeds office title deed T 9271/1988 is attached. The remaining extent of the farm Homestead no 668 will have to be subdivided to create a portion of ±116ha on which the township will be established.

The Matjhabeng Council will approve the layout at their Council meeting in November 2013 (copy of letter will be sent).

- LAYOUT PLAN (1218/DRW11)

The layout plan makes provision for 741 erven and streets that can be accommodated on this portion of vacant land. The Surveyor General will be requested to allocate erf numbers to this extension as well as the extension number once the Townships Board has recommended the layout for approval by the MEC. The layout was discussed with town planners from the Department of Cooperative Governance and Traditional Affairs (COGTA), the technical Department of the Matjhabeng Municipality and at various PSC meetings where COGTA was present and the requested amendments were made.

## RESIDENTIAL DEVELOPMENT

The proposed residential development is east and southeast of the present Homestead Thabong extension 15 and southeast of Thabong. This proposal takes up the last portion of the area that is available for township establishment purposes between Thabong ext 15, Homestead and the flood line area south of Homestead.

This area has been identified as an area for future residential development in the spatial development framework (SDF) for Masimong in the Matjhabeng IDP.

The gradient of the area is acceptable for residential development. The 1:50 and 1:100 year flood lines restrict the development of the area to the south. The 708 residential erven are on average 325-400 m² in size while some larger erven were provided on block corners to make provision for building lines. Services can be provided to the erven from the adjacent extensions.

The layout plan also makes provision for 6 higher density residential erven which can accommodate about 597 units at a density of 50 units per ha. The 6 erven can be sold on tender to developers who can be requested to submit development proposals to the Council.

## STREETS

Access to this area is from different streets from Thabong. To the north of the area is the P82/1 which will eventually follow the northern route which leads directly into Jan Hofmeyer road in Welkom. The main east west connector streets are 32m wide while the north south routes are 20m wide. Three circles have been provided. The main collector streets that will also function as the bus or taxi routes, are 16m wide. This provides enough space for vehicles to stop and to drop off or pick up passengers. The 16m street is an important collector street as it will also have to be designed in such a way that storm water can be accommodated in the street. The remaining streets are 12m wide.

The general gradient in the streets in the proposed development is on average between 1:80 and 1:250. The main streets will be provided with permanent paving in the future and the streets will also have the function to accommodate storm water as described in the next paragraph. The expected rainfall in this area will present no problems in this regard.

The Department of Roads was involved in discussions regarding the re-alignment of the P82/1 and has agreed on the proposed re-alignment subject to amendments to the access points which were implemented and supported by the KMA traffic report.

The traffic report TIS 6785.02 dated August 2013 prepared by KMA Consulting Engineers concludes in paragraph 8 on page 39:

The following conclusions can be made from the study:

a) The development is not expected to generate more than 411 trips during the morning peak hour and 638 new trips during the afternoon peak hour.

b) All analysed intersections are expected to operate at acceptable levels of service, with the exception of the intersection of the P3/2 with the P82/1, where certain lane changes are recommended to reduce delays.

c) The site development plan, with consideration of the aspects discussed in Chapter 7, is acceptable from a traffic point of view.

Based on the conclusions, it is recommended that the development be approved from a traffic point of view.

## STORM WATER/FLOOD LINES

It is important that storm water is handled properly as storm water from the steeper areas will flow faster and it needs to be contained so that no damage can occur to the streets or other properties. The 1:50 and 1:100 year flood line south of the area were determined by CSM Consulting Services on behalf of Harmony when the Masimong SDF was prepared.

Storm water from the northern areas also passes through this area from the wetlands identified to the north of the layout to the wetlands identified in the northern area of this layout.

(Please also note reference to wetlands in par 7).

## PARKS, SPORT AND RECREATION

There are 7 parks and 1 sport and recreation ground provided. The largest of the parks are to accommodate a proposed storm water channel that will accommodate storm water from north to south through the wetlands while the other parks can be developed as play and/or recreational areas. The total area for parks is 8,697ha which is equal to about 2m2 per person but if the sports and recreational grounds of 10,19ha are added there is nearly 40m2 per person provided.

## BUSINESS

Five business sites have been provided in the layout for neighborhood shops which range in size from 1390-2248m2. The shops are situated next to the main and collector streets in the layout.

The large CBD site of 9,275ha has been provided and planned for in the SDF and will function as a regional shopping complex for a large area.

## EDUCATION

Two crèche sites between 2297 and 3315m2 have been provided. The crèche sites are next to or close to main roads for easy access. According to the standards or guidelines of the Department of Education and based on their recommendation 2 lower primary school sites as well as 1 secondary school sites have been provided.

## CHURCH

Based on normal planning standards of 1 church site per 200-250 erven, 4 church sites have been provided. It is possible to use residential erven for church purposes through a consent use application.

- GEO-TECHNICAL REPORT

The firm Roadlab geo-consultants has conducted a geo-technical investigation for the proposed extension for township establishment. In their attached report 2012/240/Doc dated March 2013 the area is divided into 4 geotechnical zones (page 15). A range of foundation design and building procedures are recommended in paragraph 10 of the report:

The following geotechnical considerations that could influence the proposed

development were identified:

10.1 Site Class H2/C1 : (Stiffened or cellular raft, Piled Construction, Soil

raft), Stiffened or cellular raft of articulated lightly reinforced masonry,

Or

Piled construction – Piled foundation with suspended floor slabs with or

without ground beams,

Or

Soil raft - Remove all or necessary parts of expansive horizon to 1.0m

beyond the perimeter of the building and replace with inert backfill

compacted to 93% MOD AASHTO density at -1% to +2%  ip footings

with light reinforcement in masonry if residual movement is < 7.5mm, or

construction type appropriate to residual movements.

10.2 Excavatability: Medium excavations can be expected on site – Refer to

Annexure A. No blasting operations are foreseen. However an

excavator might need to be used with some of the harder materials.

10.3 Soil classification: The typical material found on site is silty sand with

potential heave estimated as medium, although some materials are

deemed to be low. Although it is not clear that expansive materials occur

across the entire site, Welkom is deemed to have prevalent heaving clays.

This is a factor which must be considered during the design phase.

10.4 Groundwater: No ground water was encountered during the investigation.

10.5 Stability of slopes and excavations: The sides of the test pits did not

appear to fall in; therefore the excavations appear to be stable.

10.6 There seems to be an ant problem on site with copious amounts of ants encountered in various test pits.

10.7 It is recommended that no development takes place within the 100-year flood parameter.

10.8 The site conditions seem favourable for the proposed township development, subject to the aforementioned considerations.

## LAND USE

The layout will be made subject to the land uses in Annexure F of Act 4/1984 and the conditions of establishment and title as per Annexure A.

## SERVICES STATEMENT

The Local Authority will provide the erven with services.  All services are available from the adjacent Homestead Township and the extension of the services to the new erven will not be a problem. A services report by Pula is attached. The provision of electricity is dependent on the enlargement of the local substation for which an application for funds has already been submitted. The firm FCE Consulting Engineers was appointed to compile an electrical report but was not able to get the Municipality and ESKOM to attend a meeting to discuss the provision of electricity. ESKOM has now indicated that there is no objection against this application subject to their standard conditions.

## ENVIRONMENTAL IMPACT AND WETLANDS

The company NSVT has applied for an exemption permit to establish this extension. The application will be advertised and the Department of Tourism, Environmental and Economic Affairs is expected to grant authorization for the change in land use at a later stage.

Due to certain difficulties experienced such as the wetlands report there have been delays. A wetlands report was compiled by Prof J Du Preez and the information was transferred to this layout. Discussions were held with DETEA on the wetlands and we were advised to provide a 50m buffer next to or around the identified wetlands. Matjhabeng Municipality also requested an open area for a channel to be able to allow the overflow of storm water from the wetlands to the large vlei area south of the layout.

## NOTES ON APPLICATION FORM

- The conditions for inclusion in property titles are attached as Annexure A.

- There are no servitudes that affect the layout although a new servitude will at a later stage be registered in favour of Sedibeng water for their pipeline which traverses the northern part of the layout.

## RECOMMENDATION

Application is hereby made in terms of:

- Section 20 of Ordinance 9 of 1969, for the subdivision of the remainder of the farm Homestead no 668;

- Section 8 of Ordinance 9 of 1969, for the establishment of a township Homestead extension, consisting of 741 erven and streets, as shown on layout plan 1218/DRW/11 subject to the conditions in Annexure A.

P DE BIE Pr Pln 10410

p.p. PHETHOGO CONSULTING

# Text boxes

## C   o   n   s   u   l   t   i   n   g