NQABENI/EROS/ORIBI 132kV LOOP-IN-LOOP-OUT POWERLINE

BACKGROUND INFORMATION DOCUMENT

Fig 1 Ugu District Municipality Locality Map

Fig 3 Eros/Oribi/Nqabeni 132kV Cadastral map with alternative powerline corridors

Shaded corridors not-to-scale

Fig 4 District municipality; local municipalities and alternative corridors

Fig 5 Eros/Oribi/Nqabeni 132kV Ortho-Photo map with alternative corridors

Nqabeni Substation Site coordinates: 30o3’9.67”E	30o43’14.12”S

| Title (Prof/Dr./Mr/Mrs/Ms) |  |
| --- | --- |
| First name |  |
| Surname |  |
| Organisation |  |
| Postal Address |  |
| Tel |  |
| Fax |  |
| Email |  |
| Cell |  |

Please formally register me as an interested and affected party so that I may receive further information and notification during the BA process. Circle applicable

YES 		NO

I would like to receive my notification by (tick)

| Letter |  | Fax |  | Email |  |
| --- | --- | --- | --- | --- | --- |

# Text boxes

SCOPE OF WORK

This upgrade constitutes the following activities;

- Establish 2x20MVA transformer and associated structures;

- Build an approximately 8km of Twin Chikandee 132kV line from Eros Oribi1 to Nqabeni Substation.

- Removal of the existing 10MVA

Nqabeni 132/22kV Substation

LOCATION OF THE STUDY AREA

The study area is situated along a farming area within Umziwabantu and Ezingolwezi Local Municipality. The two municipalities are part of the six local municipalities within Ugu District Municipality situated south of KwaZulu Natal province.

Width of corridor

Shaded corridor width

Nqabeni 132/22kV substation

Shaded corridor width

DESCRIPTION OF THE AREA

The study area starts from Nqabeni substation running along the existing Nqabeni/Eros/Oribi 132kV powerline ending at the Eros/Oribi 132kV powerline. Both the Nqabeni substation, Nqabeni/Erosi/Oribi 132kV powerline and alternative corridors for the proposed loop-in-out powerline can be accessed from the highway N2 and local roads. The area is characterised by sugarcane plantations, grazing lands and drainage line. Mzimkhulwana River lies outside the study area. Part of the drainage line is lined by riverine bush and it falls within the study area. The study area is undulating and is steep along the drainage line.

Study area

Width of corridor

Study area

REGISTRATION AND COMMENT SHEET

Please complete and return by fax, post or by email to:

Dudu Ngidi

Ludloko Developments

P.O. Box 22964

Southgate

Pietermaritzburg

3200

Fax: 086 570 8493

Email: dudungidi@vodamail.co.za

COMMENTS

Please write any comments, quarries, concerns and suggestions you may have on the proposed project. Please use additional page, if required.

Eros/Oribi 132kV

PURPOSE OF THE BACKGROUND INFORMATION DOCUMENT

The purpose of the background information document is to inform the public about the basic assessment (BA) process that is to be undertaken for studying potential environmental and social impacts that may occur as a result of constructing the proposed Nqabeni/Eros/Oribi 132kV Loop-In-Loop-Out powerline. The powerline will connect Nqabeni 132kV substation to Eros/Oribi 132kV powerline. In addition to providing background information about the proposed project this document will provide interested and affected parties with the opportunity to:

- Register as interested and affected parties during the public participation process

- To provide initial comments and suggestions about the proposed project

- Comment on the basic assessment report as well as the environmental management plan

BACKGROUND TO THE PROPOSED PROJECT

Nqabeni 132/22kV substation is currently experiencing very high loading due to a relatively high customer base and consequently there is limited capacity in the existing transformer for a number of planned electrification connections. To improve supply and provide better capacity on the network it is recommended that Nqabeni substation be upgraded to accommodate two 132/22kV 20MVA transformers and associated structures including a loop-in and loop-out connections that will link Nqabeni substation to Eros/Oribi 132kV powerline. The loop-in and loop-out connections are to provide reliable supply in case of one connection becoming faulty. The two transformers will be able to supply the voltage that will meet current and future load demands. The recommended upgrades will thus help allow further growth on the substation and be able to address low voltage problems experienced on some associated networks. The wolf conductor currently linking Nqabeni substation to Eros/Oribi 132kV Chikandee powerline will not be able to carry the stronger electricity that will be supplied by the two transformers at Nqabeni substation. Therefore a conductor that will be able to carry the stronger voltage is recommended. In this case the Chikandee conductor is recommended and will also be similar to the Eros/Oribi powerline conductor it will be connected to. Two alternative corridors have been investigated.

Eskom Holdings SOC Limited has appointed Ludloko Development an independent environmental consultant to apply for authorisation for the construction of the powerline and expansion of substation from relevant authority and to undertake a basic assessment study in accordance to the NEMA of 1998 EIA regulations document GNR543.

KEY LEGAL ASPECTS

R543 of NEMA (Act No 107 of 1998) states that an activity such as the proposed construction of powerline with a  capacity more than 33 but less than 275 kilovolts a listed activity in Listing Notice 1 of GNR 544, requires application for environmental authorisation to the relevant authority prior to commencement of the proposed construction of the project. A basic assessment process described in Part 2 of GNR 543 of the EIA Regulations under sections 24(5), 24M and 44 of the National Environmental Management Act, 1998 (Act No. 107 of 1998) is applied for this proposed project. This section stipulated in Part 2 of GNR 543 describes the basic assessment process for undertaking an environmental assessment.

SPECIALIST STUDIES

The need for specialist studies such as heritage, avi-fauna will be determined during the basic assessment process

OVERVIEW STEPS IN THE BASIC ASSESSMENT PROCESS

- Application form submitted to National Department of Environmental Affairs

- Affected landowners are notified about the proposed project

- DEA provides a reference number

- I&AP and relevant authorities are identified and the I&AP register is initiated

- A BID is prepared and distributed

- The proposed project is advertised in local newspaper(s)

- Public participation process is started

- Basic assessment (BA) study is undertaken together with specialist studies

- Draft copy of the BA report and a general environmental management plan are prepared

- DEA receives the copy of the draft BA report

- Registered I&AP are notified of the availability of the draft BA report and are notified of comment period of 40 days

- The BA report is placed at local library or municipality

- Comments from I&AP are sent to DEA

- Comments submitted by I&AP and authorities are compiled into a final BA report

- The final BA report is distributes for final comments  within 21 days of distribution

- Final BA report is submitted to DEA

- Registered I&AP are notified of DEA decision as well as the appeal process within 14 days of the notice on the decision

PUBLIC PARTICIPATION

The proposed project will be advertised in the local newspaper and interested and affected parties can write to the consultant mentioned in the advert and enquire about the project and also express their views about the proposed project. Relevant authorities will be notified about the project. The public will be given an opportunity to attend meetings where the proposed project will be presented, explained and discussed. At these meeting the public will express their views, concerns, comments and suggestions. Comments provided will ensure that relevant issues are evaluated during the basic assessment process. The basic assessment report will be made available to the public for perusal. The report will be placed at the local library or at municipality.

HOW YOU CAN PARTICIPATE

- By responding (by phone, fax or email) to the invitation for your participation which is attached and will appear in the local newspaper

- By mailing, faxing or emailing the attached registration and comment form to Ludloko Developments consultants

- By phoning us if you have a query, comments or requiring further information on the project

- By commenting on the draft basic assessment report within 40 days

Nqabeni/Eros/Oribi 132kV

Eros/Oribi 132kV

30o4’11.53”E	30o41’47.58”S

30o3’33.66”E	30o42’26.22”S

Project description

Two alternative corridors were investigated for the location of the powerline. Location of the corridors was determined by the location of suitable connection points along the existing Eros/Oribi 132kV powerline. The size and length of the corridor is determined by the availability of open space, terrain, land status and connection points. Preliminary investigations show that corridor 1 as shown in figures 3; 4 and 5 below. A powerline corridor by rule has a diameter of 500m and its length will cover the length of the proposed powerline. A powerline route can be selected within a designated corridor. Preliminary investigation shows that corridor 1 is suitable due its accessibility, connectivity and landowner inputs.

Corridor 2

Corridor 1

Nqabeni/Eros/Oribi 132kV

Corridor 1 - Preferred

30o3’33.66”E	30o42’26.22”S

30o4’11.53”E	30o41’47.58”S

Corridor width

Corridor width

Eros/Oribi 132kV

Nqabeni/Eros/Oribi 132kV

Corridor 2

Corridor 1

Nqabeni 132/22kV Substation

Corridor 2 - Alternative

Fig 2 SANBI BGIS Umziwabantu and Ezingolweni Local Municipalities

According to South African National Biodiversity Institute (SANBI) Biodiversity GIS map, the study area falls within an area with little natural habitat remaining and contains less threatened ecosystem

Umziwabantu LM

Ezingolweni LM

UGU DISTRICT MUNICIPALITY