| DEAT Reference No | 14/12/16/3/3/1/830 |
| --- | --- |
| Report type | Environmental Management Plan |
| Title | Proposed 132kV Nqabeni/Eros-Oribi Loop-in-Loop-out Powerline; Ugu District, KZN |
| Report status | Draft |
| Authors | Ludloko Developments cc |
| Client | Eskom Holdings Limited (Eskom Distribution Division – Eastern Region) |
| Report Status | Draft EMP submitted as part of the final basic Assessment Report |
| Date | August 2013 |

TABLE OF CONTENT

1. 	OVERVIEW OF THE PROJECT 								1

1.1 	Introduction  										1

1.2 	Description of site 									1

2. 	PURPOSE & OBJECTIVES OF THE EMP 							2

2.1 	Overall Management Objectives 								2

2.2 	Intention of the EMP 									2

2.3 	Objectives of the EMP 									3

2.4 	Dynamic document  									3

2.5 	EMP Implementation Period 								3

2.6 	Non-compliance with the EMP 								3

3. 	ROLES AND RESPONSIBILITIES IN THE IMPLEMENTATION OF THE EMP 				6

3.1 	Environmental Assessment Practitioner (EAP) 						6

3.2 	People involved in the construction, rehabilitation activities and application

of mitigation measures are: 								6

3.3 	Appointment of an Environmental Control Officer 						6

3.4 	Tasks for Project Co-ordinator/Manager 							7

3.5 	Construction Supervisor Tasks 								8

3.6 	Environmental Consultant Tasks 								8

3.7 	Eskom Environmental Practitioner 								9

3.8 	Contractor responsibilities 								9

3.8	Provision of grassing specification for and bare areas 						9

4. 	PLANNING AND DESIGN MANAGEMENT PLAN 						10

4.1 	Activities involved at planning and design of powerline involves the following factors: 		10

4.2 	Planning and Design Objectives 								10

4.3 	Consultation objectives 									10

5. 	PRE-CONSTRUCTION MANAGEMENT PLAN – PLANNING, DESIGN AND CONSULTATION STAGE  	11

5.1 	Pre-construction stage involves:  								11

6. 	CONSTRUCTION MANAGEMENT PLAN 							13

6.1 	Construction stage involves: 								13

6.2 	Construction management overall objectives 						14

7. 	COMPLETION OF WORK 									31

7.1 	Rehabilitation and maintenance 								31

8. 	OPERATION AND MAINTENANCE  								33

8.1 	Ground maintenance and safety  								33

9.	MONITORING OF EMP IMPLEMENTATION 							35

9.1 	Report on monitoring 									35

Appendix A -Audit Schedule 								36

PART 1

1. 	OVERVIEW OF THE PROJECT							CHAPTER 1

1.1 	Introduction

This Environmental Management Plan (EMP) is compiled in terms of subsection 33 of EIA Regulations promulgated under NEMA No 107 of 1998.  A Basic Assessment has been carried out and was presented in the report appearing below:

Nqabeni/Eros-Oribi Loop-in-Loop-out 132kV powerline Basic Assessment Report prepared by Ludloko Developments July 2013

1.2 	Description of site

The site is situated on the lower slopes of a hill over-looking the municipality of Ezinqoleni and Umziwabantu within Ugu District municipality south of KwaZulu Natal. The study area is intercepted by N2. Basic assessment of the study area showed that the natural vegetation is fragmented and reduced as a result of sugarcane plantation. The grasslands is dominated by Valley Bushveld and Ngongoni grass giving it an element of Savanna biome. However according to KZN vegetation Type the area is not considered vulnerable this is due to the fact that Ngongoni spreads and thrives as a result of stress such as overgrazing and irregular fire. The grassland is slowly invaded by indigenous trees caused by overgrazing. Placing of towers will take a relatively small area and will thus have minimal impact on the natural vegetation and farming. The centre of the study area is comprised of a ridge where the existing powerline is located. The ridge extends into a steep valley on the east of the ridge forming a steep drainage line. The west of the ridge is undulating and rolls into sugarcane plantations and Umzimkhulwane River to the north of the study area. The area is predominantly planted with sugarcane. Small dairy planted grass and small vegetable gardens are found within the study area. Grazing dominates the north of the study area with rural homesteads clustered in one area west of the ridge.

2. 	PURPOSE & OBJECTIVES OF THE EMP 				CHAPTER 2

The main objective of the EMP document is to provide guidance on the development and information required to implement effective management and monitoring measures for the listed priority impacts identified in the assessment process.

Description of EMP components

| Activity/Aspect | Something that an operation does in order to do business |
| --- | --- |
| List of Associated Impacts | Actual change that takes place in the receiving environment Positive and negative impacts cased by the activity |
| Possible Causes | Mechanism of change |
| Risks | Threaten licence to operate Results in costs to Eskom Results in improved/strained relations with neighbours, regulators and other stakeholders Enhance/damage corporate reputation Enable/disrupt operations Result in compliance/non-compliance to legislation or written operating standards |
| Mitigation | Specify management measure |
| Responsible | Individual responsible for the implementation of the management measure |
| Timeframe | Period the management measure to be implemented |
| Targets | Quantify the target the operation wishes to achieve through management measure |
| KPI | For monitoring performance on the extent to which targets are being achieved or objectives met |
| Monitoring | Frequency of monitoring |
| Environmental Standard Procedure | Standard or procedure that can be used to implement management measure |
| Financial provision | Providing budget for implementing of management measure |

2.1 	Overall Management Objectives

- To identify activities that are pertinent to the project cycle

- To understand associated impacts and causes

- To ensure that the risks are known and managed

- Provide effective and measurable mitigation measures

- Assign appropriate responsibilities

- Allocate reasonable timeframes

- Quantify target the operation wishes to achieve through mitigation measures

- Provide Key Performance Indicators (KPI) in order to monitor performance on extent to which targets are achieved

2.2 	Intention of the EMP

The EMP is intended to address the environmental impacts during the design, construction and operational phases of a project. Environmental protection during the entire project must always be regarded. In order to achieve this, a number of environmental specifications/recommendations are made. These are aimed at ensuring that the contractor maintains adequate control over the project in order to:

- Minimise the extent of impact during construction.

- Ensure appropriate restoration of areas affected by construction.

- Prevent long term environmental degradation.

The contractor needs to become familiar with environmental obligations that are stipulated in this document, and must be conversant of all relevant environmental legislation. The contractor should also be aware that Eskom and Environmental Control Officer will monitor the implementation of the procedures.

2.3 	Objectives of the EMP

The EMP has the following goals:

- Re-iterate and further identify construction activities that may have a detrimental impact on the environment;

- Detailing the mitigation measures that will need to be taken, and the procedures for their implementation;

- Establishing the reporting system to be undertaken during the construction.

The EMP also serves to highlight specific requirements that will be monitored during the development. Corrective action will be taken in cases where environmental impacts not have been satisfactory prevented or mitigated. The document should, therefore, be seen as a guideline that will assist in minimising the potential environmental impact of activities.

The EMP also include recommendations of the roles and responsibilities of the project proponent, environmental management team and contractors.

2.4 	Dynamic document

The EMP document is not static as new developments occur it is therefore subjected to review and updating. During the implementation of a project there is always the possibility that unforeseen issues that could arise, and thus the EMP should therefore be revised where necessary to mitigate unanticipated impacts.

2.5 	EMP Implementation Period

The EMP will focus on and operate during the whole implementation / construction period and maintenance/operational phase including decommissioning of the project.

2.6 	Non-compliance with the EMP

Outlined below are a number of steps, relating to increasing severity of environmental problems, which will be implemented.

Step 1

The ECO discusses the problem with the contractor and/or non-complying party, and all work out a solution together. The ECO records the discussion and the solution implemented.

Step 2

A serious infringement occurs and the ECO either observes it or is made aware of it. ECO notifies the non-complying party in writing, with a deadline by which the problem must be rectified. All costs will be borne by the contractor.

Step 3

The ECO shall order the contractor to suspend part, or all, the works. The suspension will be enforced until such time as the offending party(ies), procedure or equipment is corrected and/or remedial measures put in place if required. No extension of time will be granted for such delays and all cost will be borne by the contractor.

Step 4

A breach of contract may constitute the removal of a contractor and/or equipment from the site and/or the termination of the contract, whether a construction contract or an employment contract. Such measures will not replace any legal proceedings that Eskom Holdings SOC may institute non-compliance against the contractor

Outline of activities associated with the proposed powerline

| Aspect | Impact | Significance before mitigation | Mitigation provided |
| --- | --- | --- | --- |
| Use of local manual labour | Will provide jobs | High | Employment of local manual labour is recommended |
| Placing of office site location and demarcation | Placing along sensitive environment will damage those areas | Medium | To be located outside sensitive environments and demarcated To limit damage to prevent further erosion |
| Location of campsite (Optional) and demarcation | Placing along sensitive environment will damage those areas | Medium | To be located outside sensitive environments and demarcated To limit damage to prevent further erosion |
| Demarcation of construction site | Placing along sensitive environment will damage those areas | Medium | To be located outside sensitive environments and demarcated To limit damage to prevent further erosion |
| Movement of construction vehicle tracks | Can cause erosion | High | Limited to single tracks |
| Providing environmental awareness for contractor workers | Lack of information can cause more impacts | High | To make them aware of impact identification and mitigation |
| Cutting indigenous trees | For locating powerlines | Low | Permits will be sought |
| Damage to grassland | Excessive digging | Medium | All digging to be limited within demarcated area |
| Use of local roads | Indiscriminate parking or reckless driving | Low | Road by-laws are to be maintained |
| Designated storage site, smoking area, ablution | Spread of fire | High | Smoking areas are to designated and prevented from spreading fire |
| Change in landuse | Social impact |  | There will be no change in landuse |
| Soil excavation and levelling | Erosion | High | Disturbed ground around tower bases need to be grassed to prevent erosion and formation of gullies |
| Mixing of topsoil with spoil and subsoil | Polluting topsoil | Medium | Topsoil has the required nutrients for supporting new growth Topsoil to be securely stored |
| Opened of excavated holes | Livestock accidents | High | Open holes are to be closed as soon as it is possible to do so to prevent accidents |
| Use of unregistered landfill site | Pollution Illegal dumping | Medium | Liaison with municipality to use registered landfill sites |
| Encountered heritage artefacts |  | Low | All work must stop and report the heritage artefacts |
| Lack of dust control | Pollution | Low | Dust generated is small |
| Management of noise | High noise level | Low | Construction of powerline has low noise |
| Poor storage and use of chemicals & hazardous chemicals | Pollution Accidents Injuries | Medium | Storage site to be demarcated and placed on impervious and containing material |
| Poor management of waste | Pollution and littering | Medium | Waste is to be separated and disposed appropriately |
| Incident management | Pollution of natural resources Collapse of open holes | Medium | To prevent spread of pollution |
| Emergency preparedness | Accidents Injuries Pollution of natural resources and groundwater | Low | The emergency preparedness procedure should be in place and workers trained on it |
| Servicing and refuelling of vehicles | Ground pollution | Low | All vehicles should be serviced at service centres |

3. ROLES AND RESPONSIBILITIES IN THE IMPLEMENTATION OF THE EMP 		CHAPTER 3

3.1 	Environmental Assessment Practitioner (EAP)

The EAP Duduzile Ngidi is registered with South African Council for Natural Scientific Professions (SACNASP) as a Professional Natural Scientist, registration number 400033/01 in terms of section 20(3)(a) of the Natural Scientific Profession Act, 2003. The EAP has over 10 years experience in the EIA field. The EAP has the following experience:

- Good theoretical training and practical experience on undertaking Environmental Impact Assessment (EIA) study, execution of the EIA plan of study and EIA project management, this include:

- Knowledge of environmental legislation and regulatory requirements and their incorporation into the EIA process

- Understand and able to present the business case for the EIA projects to stakeholders and able to incorporate the business case in the EIA report

- Good understanding of impact assessment methods, from simple checklist to complex calculations

- Good command of analysing technical information and communicating it to project team and stakeholders

- Sound knowledge of the compilation of Environmental Management Plans/programmes (EMP) report based on the findings of the EIA study, including synthesis and incorporation of recommendations from specialist studies

3.2 	People involved in the construction, rehabilitation activities and application of mitigation measures are:

- Project manager and coordinator

  - Project management and project time frames

- Construction supervisor

  - Construction and safety monitoring

- Resident environmental control officer

  - Appointed to monitor and record compliance and non-compliance to the ROD conditions and to other relevant legislation and application of the EMP

- Eskom environmental practitioner

  - To monitor compliance

- Environmental consultant

  - Compile the EMP

  - Distribute EMP to authority, contractor and project engineer

- Community liaison officer

  - To liaise with the community

  - To note and keep a record of community concerns and questions

  - To ensure addressing of the concerns

3.3 	Appointment of an Environmental Control Officer

An Environmental Control Officer has been created to ensure that the mitigation measures and other requirements set forth in the EMP are adhered to. It is recommended that Eskom appoint an independent Environmental Control Officer (ECO) during the construction phase of the project.

The following guidelines apply to the functions of an ECO:

- The ECO should be conversant and has full understanding of the contents of the Environmental Management Plan

- The ECO should and explain the EMP to the contractor, the site staff, the supervisors and any other relevant personnel or I&AP’s.

- The ECO would have to be on site on a regular basis – preferably once a month to supervise environmental actions associated with construction activities.

- The ECO should be able to understand, interpret, monitor, audit and implement the EMP.

- The ECO must then give feedback of the audits to Eskom and Contractors. This must be in the form of a written report

- The ECO must ensure that the contractor understands what is to be done to rectify and address any problems that have arisen from the audit.

- Be familiar with environmental and other related legislation including contraventions and penalties

- Attendance at scheduled project meetings

- Monitor the contractor’s compliance with the EMP on site

- Conduct monthly observation and environmental audits of all work areas

- Check of all completed work (storage of topsoil, its application, grassing etc)

- Keep all records of project monitoring for audit

- Be responsible for all environmental communication on the project with the project team

- Discuss queries from I&AP

- To channel/direct all public statement on environmental issues to Environmental practitioner

- Discuss content of the EMP with construction supervisor and with Project management

- Monitor compliance to ROD and EMP recommendations

- Attend to environmental incidents and liaise with construction supervisor to implement prevention measures

- Keep a regular photographic record of all environmental incidents

- Report environmental incidents to Eskom Environmental Senior Advisor and to Environmental Practitioner assigned to the project

- Liaise with Drizit (Oil and Chemical Management Specialists) on correct management procedures. Contacts provided in section 12 end of document

- Attend on-site meetings

- Bring to the attention of project team environmental related problems and report on progress

- Check quality of rehabilitation work

- Discuss poor quality with construction supervisor and ensure proper implementation of procedures

- Ensure that all sub-contractors and other workers appointed by the Contractor are complying with, and implementing the construction EMP during the duration of their specific contracts

- Provide environmental practitioner with progress reports

- Approve completion of each rehabilitation work

3.4 	Tasks for Project Co-ordinator/Manager

The project manager will be responsible for ensuring that the EMP and associated documents are compiled with the contractor.

- Be familiar with the content of the EMP

- Discuss the EMP report with the project team

- Monitor the Contractor’s compliance with the Environmental Specifications and enforce compliance

- Liaise with Eskom Environmental practitioner

- Notify landowners and local municipality about project schedule and activities prior to construction

- Undertake damage assessments where incidents, accidents and serious infringements have occurred on or a relevant distance off site

- Notify landowners prior to entering private property

- Assist with the appointment of Environmental Control Officer (ECO) and Community Liaison Officer (CLO)

- Monitor progress and environmental issues associated with the project

- Ensure that all environmental recommendations are implemented and adhered to

- Ensure that there is adequate finance for environmental incidents that need to be corrected

- Record and report environmental incidents to Eskom Senior Environmental Advisor

- Implement Temporary Work Stoppages where serious environmental infringements and non-compliance

- On completion of the project, ensure that the community and other stakeholders are satisfied with the state of their area

- Become involved in the EMP process and make necessary changes or modifications to the EMP

- Ensure that damages to property and land are addressed to the satisfaction of the landowner

- Ensure that all damage and servitude acquisition compensations are paid

- Chair any environmental incident and environmental non-conformance enquiries

3.5 	Construction Supervisor Tasks

- Implement the recommendations of the EMP document

- Ensure adherence to safety standards and procedures as stipulated in the Contractor Project Quality Assurance file containing Safety, Health and Environment (SHE) standards

- Ensure induction material includes project appropriate environmental issues

- Discuss appointment of ECO and CLO with the project manager/coordinator

- To liaise with ECO on compliance and completion of rehabilitation tasks

- Purchase all necessary and correct rehabilitation material; to be delivered on-site in time

- Monitor the application of rehabilitation specifications for powerline construction such as

  - Grassing of disturbed and denuded areas (along the powerline, , vehicle tracks and campsite)

  - Cutting of identified trees along the powerline servitude

  - Application of herbicides to stumps

  - Construction of access roads

  - Creation of a temporary cement slurry holding pan

  - Disposal and removal of construction waste

- To have knowledge of the contents of the “Procedure for vegetation clearance and maintenance within overhead powerline servitudes and on Eskom owned land” document. The contractor and the ECO are to have knowledge of the content of the document and are to discuss the content with the construction staff.

- Maintain site documentation related to environmental management (permits, EMP methods, ROD, audit reports, waste removal etc) Documentation to ne maintained on the relevant site Document Control System

- Provide emergency procedure for environmental incidents

3.6 	Environmental Consultant Tasks

- To disseminate the ROD to all relevant parties

- To prepare EMP report and distribute to project manager

- To liaise with DWAF about cutting of indigenous trees along powerline servitude

- To provide special grassing specification

- To provide clarifications on any queries based on the EMP

3.7 	Eskom Environmental Practitioner

- To assist in dealing with environmental incidents

- To ensure that quality work has been done

3.8 	Contractor responsibilities

- Be familiar with the contents of the EMP and the specifications contained herein

- Comply with the Environmental Specifications contained in the EMP and subsequent revisions

- Confirm legislative requirements for the construction works, and to ensure that appropriate permissions and permits have been obtained before commencing activities

- Prepare Method Statements, programme of activities and drawings/plans for submission to the RE (and ECO); when requested

- Undertake daily site inspections to monitor environmental performance and conformance with the Environmental Specifications

- Notify the ECO and RE immediately in the event of any accident or infringements of the Environmental Specifications and ensure appropriate remedial action is taken

- Notify the ECO and at least 10 working days in advance of any activity he has reason to believe may have significant adverse environmental impacts, with specific reference to blasting, so that mitigatory measures may be implemented timeously

- Ensure environmental awareness among his employees, sub-contractors and workforce so that they are fully aware of, and understand the Environmental Specifications and the need for them

- Maintain a register of environmental training for site staff and sub-contractor’s staff for the duration of the contract

- Undertake rehabilitation of all areas affected by construction activities to restore them to their original states, as determined by the RE and the ECO

- Rehabilitating services, utilities, private/public property and other areas adversely affected by construction activities outside of demarcated areas

- Communicate and liaise with the RE / Site Manager and the ECO to ensure effective, proactive environmental management with the overall objective of preventing or reducing negative environmental impacts while enhancing positive environmental impacts

3.8	Provision of grassing specification for and bare areas

The contractor will appoint an independent landscaper. Use of landscapers familiar with landscaping requirements for the area will be an advantage. The contractor needs to discuss the grassing specification with the landscaper. The contractor needs to provide a grassing contract with clear deliverables. All planting should take when there is little chance of the planted material being disturbed by staff and construction vehicles. The landscaper is responsible for:

- Providing grassing specification suitable for the area

- Discussing the grassing specification as indicated on the drawing plan

- Indicate whether the planted material will need to be watered

- Ensure safe storage of grassing material before planting

- The percentage of grass cover at hand over to contractor must be decided between the contractor and the landscaper

PART 2

4. 	PLANNING AND DESIGN MANAGEMENT PLAN 				CHAPTER 4

4.1 	Activities involved at planning and design of powerline involves the following factors:

- Incorporate inputs from the basic assessment study including inputs from various stakeholders

- Identification of a site that will have minimal environmental constraints

- Identification of a site that will require minimal earthworks

- Location that will not affect people such as relocation

- Establishing fixed site parameters

- Will not involve significant change in landuse and landscape

- Is accessible and may not involve major construction of access road

- Design that will not affect fauna

- Design that will not pose environmental degradation

- Design that is safe and has a system that has a shut-off mechanism in case of breach of safety

4.2 	Planning and Design Objectives

- To capture environmental considerations early in the project cycle

- To ensure that the planning and design ensure environmental protection

- Provide activities that will reduce rehabilitation costs thus maximising compliance

- Ensure that social benefits are maximised

- To provide reliable quality of supply

- Provide technology that will reduce proliferation of areas with massive highly visible structures that may disturb the visual character of the area and sterilise vast lands

4.3 	Consultation objectives

- To provide opportunity for stakeholders to engage effectively

- To build relationship with stakeholders

- To communicate about the operation

- To gather information on issues

Mitigation measures are presented in this section of the report to provide measures that will reduce, limit, eliminate or compensate for impacts, to acceptable/insignificant levels. Consideration has been taken to ensure the practicality of implementing the measures. Inclusion of environmental recommendations during planning and design of the project has shown to not only to reduce rehabilitation costs but may eliminate costly project delays and avoid bad publicity as a result of environmental negligence or non-compliance. Environmental recommendations for planning and design should be presented to the project engineers prior to the commencement of construction

Designing for the project layout plan should include the appropriate locating of all construction areas including camp site, worker accommodation camps (where required). A site layout plan will include the following:

- Site access (including entry and exit points);

- Material and equipment storage areas, including storage areas for hazardous substances such as fuel and chemicals

- Construction office site, parking areas and staff place at the construction site

- Fencing of the construction site, camp site and parking site

- Areas where vegetation will be cleared

5. 	PRE-CONSTRUCTION MANAGEMENT PLAN – PLANNING, DESIGN AND CONSULTATION STAGE 						CHAPTER 5

5.1 	Pre-construction stage involves:

List of associated impacts at this stage are based on data sourced from strategic environmental assessment or from other existing high level data such as data from Spaceman map and through public participation

Objective: To minimise potential environmental risks at early stages of project cycle (planning and design) stage

| Activity/Aspect | Lack of environmental input in planning and design Design that does not fit into the site footprint Poor infrastructural design |
| --- | --- |
| List of Associated Impacts | Environmental degradation Unsafe operation Negative impacts on people Affect landuse Impact on cultural and landscape character Site footprint extending on private property Affect property borders Intrusion on private property |
| Possible Causes | Lack of proper planning Location on sensitive environments Unstable structures as a result of poor design Relocation of people Location on important landuse and cultural sites Lack of proper consultation |
| Risks | Non-compliance and fines Disruption of interconnected ecosystems and sensitive habitats Emotional stress on affected people Irreversible destruction of landscape and cultural sites Compromising safety standards Disruption on electricity supply as a result of poorly constructed structures |
| Mitigation | Identify environmentally suitable and stable corridor area Ensure that appropriate authorisation of design structures is done Liaise with stakeholders and interested and affected parties to ensure that the location is acceptable Location of access road within the defined servitude Incorporating geotechnical recommendations that will minimise impact on receiving surface and sub-terrain land and erosion control Finalise the location of the site in relation to associated infrastructure components such as incoming and outgoing lines Incorporate recommendations from strategic environmental assessment (SEA) Planning and design must fit the receiving environment and ensure minimal disturbance Planning location of project site, campsite, vehicle parking bay, office site, storage area (for topsoil, rubble, construction material) and cement mixing area Plan for use of manual labour and skills transfer where possible Provide mentoring on skills transfer, if possible |
| Responsible | Project Engineer, Project Surveyor and Environmentalist |
| Timeframe | Prior to construction and during negotiations with stakeholders |
| Targets | Avoidance of sensitive environmental sites Proof of comprehensive public participation Approval of project set-up (plan and design) internally and externally No change in site footprint and access road servitude once established unless approved by affected landowner(s) Evidence of consideration of geotechnical information where applicable |
| KPI | Evidence of communication with all registered stakeholders and I&AP Show the map showing proper site footprint Design structural illustrations approved by all relevant persons Report from geotechnical engineer available and incorporated |
| Monitoring | To be done prior to construction upon completion of planning and design to ensure that all authorisation is in accordance and that all consultations have taken place and that all strategic issues have been considered |
| Environmental Standard Procedure | None |
| Financial provision | Rehabilitation costs for potential environmental damage are to be included into the overall project costs, to ensure that financial resources are available when required |

6. 	CONSTRUCTION MANAGEMENT PLAN 					CHAPTER 6

6.1 	Construction stage involves:

- Establish and demarcation work area parameter

- Site security

- Liaising with Ward Councillor, about use of manual labour

- Check for nearest registered waste site

- Location of office site

- Water connection point if available

- Construction staff camp site or use of local accommodation to accommodate staff

- Vehicle parking site

- Mobile toilet site

- Safe smoking area

- Undertaking of environmental awareness with construction staff

- Environmental incident register

- Provision of marked waste bins (domestic, recycled material)

- Erection of perimeter fence to contain work area and as a safety requirement

- Posting of all safety signs along access road and along main site gate

- Removal and storage of topsoil

- Indicating and marking of access road

- Establish temporary drainage

- Removal and storage of topsoil

- Soil excavation

- Site levelling

- Construction of banks

- Levelling of access road to channel run-off out of the road

- Site compaction

- Construction of cut-off and vee-drains and outlet drains fitted with dissipaters

- Application of approved herbicides on the high voltage site

- Removal of rubble to a registered waste site

- Behaviour of construction staff in the area

- Prevent damage of local fences

- Stabilisation of banks

- Removal of construction rubble and scrap metal

- Grassing of bare areas

6.2 	Construction management overall objectives

- To ensure that mitigation measures for all identified potential impacts are provided

- To ensure that mitigation measures are applicable and effective against identified impacts

- To ensure that project environmental awareness is communicated to the involved staff

- To ensure that site specific measures are applied

- To ensure that disturbed areas are rehabilitated accordingly

- Where damage occurs outside the site, that the damage is recorded an d compensations accordingly

- To ensure that emergency preparedness is in place in order to contain consequences of the emergency situation

Location of alternative camp sites should be placed away from existing drainage lines and away from nearby streams. Use of land for locating campsite, vehicle parking bays outside the site footprint should be discussed with the landowner. Use of available water is to be discussed with affected landowner or relevant authority (municipality of DWA)

CONSTRUCTION SITE

Objectives: 	To minimise damage along the construction site

To ensure site plans, procedures and standards are in place

| Activity/Aspect | Activities within construction site |
| --- | --- |
| List of Associated Impacts | Erosion Littering Pollution Property damage Vegetation clearing |
| Possible Causes | Indiscriminate removal of vegetation Poor stabilisation of disturbed areas Lack of provision of waste bin Lack of waste management plan Poor demarcation of work area |
| Risks | Loss of topsoil Non-compliance to applicable legislation Damage to private properties Disputes and conflicts with landowners Damage to Eskom reputation |
| Mitigation | No fauna or wild animals may be collected or poached or hunted or killed, trapped or injured in any way No indiscriminate destruction of fences or access to adjoining properties is regarded as a criminal offence and shall be handled and treated as such Work must be restricted within the demarcated construction site All wastes generated on site must be properly separated, contained and disposed of Recycling, waste avoidance and minimisation shall be carried out as far as is practicable Potable water must be provided |
| Responsible | Construction supervisor, Construction manager, Project Engineer and ECO |
| Timeframe | During construction |
| Targets | No littering Visible site demarcation Presence of waste management equipment No damage to private property |
| KPI | Compiled site waste management plan Documented incident register Documented incident management plan |
| Monitoring | Monthly |
| Environmental Standard Procedure | Waste management Eskom Entering private properties procedures |
| Financial provision |  |

USE OF MANUAL LABOUR

Objective: To provide needed job opportunities. To provide exposure to technical skills (if permissible)

| Activity/Aspect | Provision of temporary employment and skills transfer where possible |
| --- | --- |
| List of Associated Impacts | Benefits to local community Disappointment with disregarding of use of manual labour |
| Possible Causes | High unemployment Desperation in need of any temporary work Strongly expected by community |
| Risks | May result in tension Bad publicity for Eskom and contractor Disruption of work, loss of man-hour |
| Mitigation | Actively involve local municipality and ward councillor in recruiting people for manual labour Skills transfer to be done where possible Discuss skills transfer plan with local municipality and ward councillor Limit access into the construction site only to the employed and trained construction staff |
| Responsible | Contractor, local municipality and ward councillor |
| Timeframe | During construction |
| Targets | Agreed upon number of temporary employment Agreed upon number on skills transfer |
| KPI | Record of temporary employment and skills transfer Evaluation form of skills transfer |
| Monitoring | Daily |
| Environmental Standard Procedure | None |
| Financial provision | Skills levy or skills coupons |

ENVIRONMENTAL AWARENESS

Objective: To improve environmental awareness and thus prevent unnecessary damage and pollution

| Activity/Aspect | Environmental awareness to all construction staff |
| --- | --- |
| List of Associated Impacts | Environmental damage and degradation Exacerbation of damage due to lack of knowledge |
| Possible Causes | Lack of environmental knowledge Lack of awareness on content of EMP document |
| Risks | Irreversible damage Fines and possible litigation Incremental damage |
| Mitigation | The project co-ordinator is to read the EMP report and ensure that construction staff and the on-site construction supervisor have read the report or are aware of the recommendations in the report. All site staff shall be made formally aware of the contents of this EMP and its conditions Environmental awareness should involve identification of environmental risk and presentation of corrective measures for each identified environmental risk |
| Responsible | Project manager |
| Timeframe | Daily during toolbox talk |
| Targets | Zero damage by staff to the receiving environment No reporting of lack of knowledge on environmental issues |
| KPI | No damage resulting from staff actions as a result of ignorance |
| Monitoring | Daily |
| Environmental Standard Procedure | Induction tape or talk |
| Financial provision | Funds to be made available as per damage |

ESTABLISHING CAMPSITE AND OFFICE SITE

Objective: To miminise impacts associated with the establishment and operation of construction and camp sites. To minimise and control damage to receiving environment and to entrench accepted behaviour amongst communities construction work in

| Activity/Aspect | Establishing campsite, office site, vehicle parking bay and construction material storage area |
| --- | --- |
| Potential impacts | Loss of ground cover due to clearing Creation of a temporary access road Uncontrolled movement of run-off from temporary water tap Oil leaks from standing vehicles Oil leaks from serviced vehicles on site Waste pollution Unsafe storage of construction material Uncontrollable management of chemical leaks due to improper storage Pollution of nearby streams or drainage lines Illegal use of land for locating campsite or vehicle parking bay Improper behaviour by construction staff with residents Spread of fire from the site or through the site due to lack of fire belts |
| Possible Causes | Lack of proper planning at planning and design stage Soil erosion Creation of water gullies from uncontrolled run-off Lack of discipline to collect waste daily Lack of planning for campsite, vehicle parking site, office site and storage sites Lack of placing impermeable moulds to contain vehicle oil leaks Uncontrolled storage of construction material Lack of education on good behaviour supported by contractor worker policy and health issues |
| Risks | Water and soil pollution Permanent loss of topsoil Waste carried by winds and polluting neighbouring properties Explosion of hazardous material and inability to control the explosion due to inaccessibility as a result of being covered by other heavy construction material Litigation and conflicts as a result of using land illegally Health problems in the community caused by improper behaviour from construction staff Spread of human transmittable diseases Loss of property and assets due to run-away fire Bad reputation on Eskom and contractor Loss of business by contractor Non-compliance to municipality by-laws such as creation of fire belts |
| Mitigation | Proper consultation for use of new land for establishing a camp site Site camps shall be properly fenced and adequately demarcated Firebreaks should be established around the construction site, camp site (where applicable), around vehicle parking bays (where applicable) and around office site (if outside construction site) A fire-break shall be cleared and maintained around the perimeter of the site including office site No open fires are permitted in the field, except under strictly controlled conditions and subject to the statutory requirements of local ordinances and the National Veld and Forest Fire Act, 1998, (No. 101 of 1998) Provision must be made for adequate chemical sanitation facilities All conditions incorporated in the requirements of the Occupational Health and safety Act shall also be implemented Camp site, office site, and construction site must be fenced off to clearly demarcate the sites and contain all activities within the sites Notices must be posted on the fences and gate of the construction site to make the members of the public aware of activities and safety issues Drainage run-off channelling system is to be constructed to channel runoff from areas of potential pollution, e.g. vehicle maintenance area, chemical and fuel stores, etc into constructed separation sumps No littering or dumping of solid waste of any description is permitted on the site. All litter, especially plastics, as well as other material capable of being dispersed through the surrounding veld and constituting a hazard to adjacent farming activities shall be regularly collected, at least on a daily basis, and properly stored prior to disposal to an approved site Upon completion of construction work the camp site must be fully rehabilitated by removing the temporary surface, ripping the area to loosen the soil and rehabilitating according to the landscape development plan for the project |
| Responsible | Project manager, ECO and EEO |
| Timeframe | Before construction and during operation |
| Targets | No use of new land without authorisation Proper and effective plan showing planning for location of campsite, vehicle parking bay and office camp Zero waste on site, campsite, office site and neighbouring properties No sign of oil pollution on soil No complaints from community about misbehaviour of construction staff |
| KPI | Proof of authorisation for use of land Proof of plan for campsite, vehicle parking bay and campsite Extent and records of pollution |
| Monitoring | Daily and monthly |
| Environmental Standard Procedure | Management of oil pollution Establishing of firebreaks according regional requirements |
| Financial provision | Provision of funds for rehabilitation of spoiled soils and/or cleaning of oil polluted water |

DEMARCATION OF SITE AREA

Objective: To limit potential damage within site footprint thus reducing rehabilitation costs and preventing damage to neighbouring properties

| Activity/Aspect | Demarcation of the site area and access road |
| --- | --- |
| Description of neighbouring sites | Neighbouring sites comprise of grazing land west of the site and residential area south of the site. The site has a gradual slope |
| List of Associated Impacts | Limits construction activity within site footprint thus minimise unnecessary damage Limits work within authorised area thus preventing illegal encroachment of neighbouring properties Degradation of temporary access roads during heavy rains due to heavy vehicles Creation of passing bays for heavy vehicles along small local roads to allow passage of on-coming traffic Uncontrolled smoking areas leading to spread of fire |
| Possible Causes | Compliance to legal requirements for site acquisition Elimination of ambiguity with regards to site boundaries thus containing construction work Staff ignorant of potential impacts and how they can be managed are likely to cause damage, pollution and environmental degradation |
| Risks | Damage to neighbouring properties Damage to sensitive neighbouring properties and landuse thus increasing rehabilitation and compensation costs Bad relations with neighbours |
| Mitigation | Site footprint to be demarcated using construction tape and subsequent erection of perimeter fence where applicable Activities outside site area such as movement of construction vehicles be limited to designated area All neighbouring natural areas such as bush, open grasslands, drainage lines, grazing areas etc are to be demarcated and protected from disturbance Access to the site shall be by means of approved access roads only No unauthorised access or haul roads are permitted The Contractor must place appropriate warning signs at the entrances / exits to the, as well as at all level crossings The last mentioned signs shall be in addition to the normal signage present at “private” level crossings and shall indicate to road users the nature of the activity occurring in the immediate site vicinity as well as the presence of train traffic All disturbed areas are to be rehabilitated accordingly Before commencing with any work, all staff members will be appropriately briefed about the EMP and relevant occupational health and safety issues Educating staff about the content of the EMP will help with understanding all potential environmental risks, consequences of such risks and provide knowledge on how environmental risks can be avoided, minimised, prevented and controlled Rehabilitate temporary access roads to a better and stable state Rehabilitation of local roads to a better or stable state Rehabilitation of passing bays to the satisfaction of the affected landowner(s) |
| Responsible | Project manager |
| Timeframe | At the onset of construction |
| Targets | No area outside work is significantly disturbed by work activities Where disturbed such as local roads, rehabilitation plan should be in place and implemented All staff to take part in environmental risk assessment Complete fencing of site area where applicable All work area marked with safety tape Communication of safety with neighbours where possible |
| KPI | Level of damage on areas out of work area disturbed by work activities Significance of damage |
| Monitoring | Weekly by project manager and monthly by ECO |
| Environmental Standard Procedure | Eskom risk assessment form |
| Financial provision | Funds made available for erection of fence |

CONTRACT AREAS

Objective: To protect local fauna, flora and other natural resources from illegal use, pollution and exploitation

| Activity/Aspect | Use of contract areas and natural resources |
| --- | --- |
| List of Associated Impacts | Pollution of watercourses and neighbouring areas Spread of fire from indiscriminate disposal of cigarette stumps Cutting of indigenous and/or protected tree species Illegal hunting of fauna Disturbance to biodiversity Collection of medicinal plants Illegal harvesting/use of natural resources Harvesting and/or collection protected species Disturbance of ecosystem balance Destruction of habitat Introduction of weeds |
| Possible Causes | Lack of knowledge on use of environmental resources by contract staff Need for firewood due to lack of alternative safe cooking devises at designated areas Disregard of work policies and rules Show of lack of discipline Deliberate contravention of law due to greed Lack of respect of private property |
| Risks | Bad reputation to Eskom Bad reputation of Eskom contract workers Bad publicity of Eskom Contravention of legislation Fines and litigation Loss of future work in Eskom by contractor |
| Mitigation | Project engineer provide a plan showing the site plan The plan must indicate access roads to be used, construction lay-down areas, materials storage and delivery requirements, contractors’ offices, operational demarcation, smoke area A material delivery and storage area should be demarcated All material and equipment storage areas (including storage areas for hazardous substances such as fuel and chemicals). Construction offices and other structures. Allocation and location of waste bins Storm water control measures Demarcation of smoking areas Provision of water and temporary ablution facilities. Only designated areas may be used for the storage of materials, machinery, equipment and site offices. The site offices should not be sited in close proximity to steep areas, as this will increase soil erosion Offices (and in particular the ablution facilities, aggregate stockpiles, spoil areas and hazardous material stockpiles) must be located as far away as possible from any watercourse The Contractor shall provide adequate facilities for construction staff so that they are not encouraged to use natural resources from surrounding natural environment to supplement their needs Collection of firewood and medicinal plants is not permitted Hunting is forbidden The use of rivers and streams for washing of clothes is not permitted The use of welding equipment, and other bare flames where veld fires constitute a hazard. Indiscriminate disposal of rubbish or construction wastes or rubble is not permitted Littering of the site is prohibited Spillage of potential pollutants, such as petroleum products is not allowed Poaching of any description is illegal Use of surrounding veld as toilets is strictly forbidden Burning of wastes and clearing of vegetation is prohibited Concrete may not be mixed directly on the ground. No mixed concrete may be deposited directly onto the ground prior to placing Cement is to be mixed on impermeable material such hard wooden planks or any suitable material Starting of fire is strictly not allowed on campsite and construction site Fire fighting equipment and material shall be supplied at all sites and located at accessible areas A sufficient firebreak must be constructed to prevent spread of fire Site must be kept neat and clean at all times |
| Responsible | Project manager, Project Construction supervisor and ECO |
| Timeframe | During construction and operation stages |
| Targets | No collection of natural resources from surrounding natural areas Smoking only in designated areas Zero waste along office and campsites Sorting of waste |
| KPI | Number of incidents of illegal poaching, collection of firewood or plants, smoking in undesignated areas Records of waste management |
| Monitoring | Monthly |
| Environmental Standard Procedure | Waste management |
| Financial provision | Funds for rehabilitation |

NOISE

Objective: To keep noise within acceptable levels at all times. To notify neighbouring people of scheduled loud noises

| Activity/Aspect | Reduction of noise |
| --- | --- |
| List of Associated Impacts | Nuisance and irritation Disturbance of peace and ambience of the area Disturbing resting people in the neighbouring community |
| Possible Causes | Un-serviced construction equipment and vehicles Lack of informing neighbours of noises higher than acceptable limits if they will occur at arranged periods during construction |
| Risks | Fines Stopping of work to negotiate noise periods Bad relations between contractor and site neighbours |
| Mitigation | Machinery and vehicle silencer units are to be maintained in good working order Noisy machinery and / or vehicles must not be allowed on site until they have been repaired Noise levels must be kept within acceptable limits for neighbouring residents Inform neighbours of scheduled higher noise levels Working hours must be restricted according to the municipal noise bylaws Construction activities must only be conducted during daylight hours Local council must be informed if work is to be done on Sundays or during public holidays |
| Responsible | Contractor |
| Timeframe | Prior to making noise e.g., rock blasting |
| Targets | Maintain noise to acceptable levels No loud unacceptable noise without prior notification |
| KPI | Records of high noise levels and corrective measures |
| Monitoring | Daily |
| Environmental Standard Procedure | None |
| Financial provision | None |

STORAGE OF TOPSOIL

Objective: To prevent loss of topsoil and thus avoid subsequent excessive costs

| Activity/Aspect | Excavation & storage of topsoil |
| --- | --- |
| Potential impacts | Disturbance of ground cover Movement of soil Loss/wash-away/blown away of loose soil under high winds and heavy rains especially stored topsoil Mixing of topsoil with subsoil Illegal dumping of excess subsoil and topsoil |
| Possible Causes | Lack of plant cover Lack of bund walls or sumps to contain wash-away soil before re-application Lack of separation of topsoil from subsoil Construction during rainy season |
| Risks | Loss of topsoil Pollution of neighbouring properties by was-away soil Clogging of nearby streams or drainage lines by was-away soil Damage of banks and loss of soil used to construct banks Increased soil replacement costs |
| Mitigation | It is highly recommended that excavations must not stand open longer period of times without proper security preferably they must be closed as soon as possible Materials needed to close excavated holes need to be readily available to prevent them remaining open for long periods Excavations must be marked with tape to clearly demarcate the area and warn against access Removed soil is to be used to backfill areas where required Deficiency of backfill material will not be made up by excavating illegally Imported backfill material should be purchased from legally registered merchandise Excess soil resulting from levelling activities of the work area should be stored in low heaps either on the access road or already disturbed area Topsoil is to be stripped together with grass / groundcover from all areas where permanent or temporary structures are located, construction related activities occur, and access roads are to be constructed Topsoil is to stored separately from subsoil and construction rubble Topsoil is to be placed away from vehicle movement Bund walls made of earth are to be constructed around or along topsoil mounds to help contain wash-away soil during heavy rains Topsoil is to be watered to help sink it and prevent being blown away Emergency preparedness for addressing potential loss of topsoil Used of crushed stones and soil binding material on access roads to control potential erosion |
| Responsible | Project manager and project supervisor |
| Timeframe | When necessary |
| Targets | Zero loss of topsoil Separation of topsoil from subsoil and/or rubble Existence of bund walls Existence of an emergency preparedness in case of heavy rains |
| KPI | Extent of loss of topsoil Storage status of topsoil |
| Monitoring | Weekly |
| Environmental Standard Procedure | None |
| Financial provision | Funds to purchase imported topsoil |

HERITAGE ARTEFACTS

Objective: To sensitise construction staff on heritage artefacts including embedded objects or human bones on construction site

| Activity/Aspect | Encountering heritage artefacts |
| --- | --- |
| List of Associated Impacts | Discovery of valuable heritage artefacts Good publicity for Eskom for contribution to heritage protection and reporting Damage and destruction of heritage assets Non compliance to heritage act |
| Possible Causes | Lack of knowledge about heritage artefacts by construction staff Lack of observation by construction supervisor Accidental damage during excavation |
| Risks | Fines and litigation Bad publicity Loss of future work from Eskom by contractor for continued damage to artefacts |
| Mitigation | The Contractor shall arrange for Environmental and Heritage Awareness Training programmes for the personnel on site Amafa AkwaZulu Natali should be contacted if any graves are identified during earthmoving activities and all development should cease until further notice Amafa AkwaZulu Natali should be contacted if any heritage objects are identified during earthmoving activities and all development should cease until further notice. If an artefact on site is uncovered work in the immediate site should be stopped immediately and the ECO shall be notified as soon as possible Contractor shall take reasonable precaution to prevent any person from removing or damaging any such article. Work shall resume once clearance is given in writing by an appointed archaeologist. |
| Responsible | Project manager, Project supervisor, ECO EEO |
| Timeframe | Daily during construction |
| Targets | Quick recognition of archaeological artefacts Minimal damage to archaeological artefacts Reporting on encounters Reporting on corrective actions taken |
| KPI | Documentation on findings Records of corrective measures taken Application of recommendations from archaeologist |
| Monitoring | Daily during construction |
| Environmental Standard Procedure | None |
| Financial provision | None |

DUST CONTROL

Objective: To control occurrence of dust along construction site

| Activity/Aspect | Dust control |
| --- | --- |
| List of Associated Impacts | Air pollution Dust entering neighbouring properties Poor visibility Health implications |
| Possible Causes | Dust resulting from earthworks, excavations, disturbed bare areas such as tower bases and other bare areas Movement of vehicles along local gravel road and access road and around/within construction site |
| Risks | Complaints from affected individuals Compensation for damage caused by dust Complaints on experiencing breathing problems Accidents due to poor visibility Stopping of work Loss of work time |
| Mitigation | Water must be applied when necessary on areas where dust may occur Dust levels on site must be kept low at all times Water to control dust must be available when needed Permission to extract water from nearby streams must be requested from Department of Water Affairs (DWA) Use of crushed stones and soil binding material on access roads to minimise dust |
| Responsible | Project manager and project supervisor |
| Timeframe | During construction |
| Targets | Zero dust levels No complaints about dust problems from neighbouring community |
| KPI | Amount of dust observed daily Recorded dust levels and reported to ECO |
| Monitoring | On a daily basis by project manager and project supervisor |
| Environmental Standard Procedure | None |
| Financial provision | Funds for transporting water needed to control dust |

CONSTRUCTION OF ACCESS ROAD

Objective: To prevent erosion and degradation

| Activity/Aspect | Creation of access road to tower bases |
| --- | --- |
| List of Associated Impacts | Erosion Scouring of road surface and adjacent area due to uncontrolled run-off Affecting of other road users due to poor road surface |
| Possible Causes | Poor construction of access road Lack of effective road gradient to channel run-off, off the access road thus prevent formation of water pools that lead to surface damage Lack of outlet drains along the road Poor access road planning |
| Risks | Erosion of access road Inability to drive and impacting on maintenance of powerline Increased rehabilitation costs |
| Mitigation | Addition of crushed stones and soil binding material to prevent potential erosion Proper construction of access road according to the road construction design Soil moved during construction of the soil to be disposed properly |
| Responsible | Project manager, ECO, Eskom Environmental Officer (EEO) |
| Timeframe |  |
| Targets | Zero erosion of access road No sign of loose soil No signs of dips along the road Good outlet drains |
| KPI | Erosion incidents Status of road Proper outlet drains |
| Monitoring | Monthly |
| Environmental Standard Procedure | Road construction specification |
| Financial provision | Funds to rebuild poorly constructed access roads |

ENVIRONMENTAL INCIDENTS AND EMERGENCY PREPAREDNESS

Objective: To be prepared for any environmental incident and to be able to control it

Environmental emergency procedures ensure that there will be an appropriate response to unexpected or accidental actions or incidents that will cause environmental impacts, throughout the life cycle of the project. Such incidents may include, inter alia:

· Accidental discharges to water and land;

· Accidental exposure of employees to hazardous substances;

· Accidental veld or forest fires;

· Accidental spillage of hazardous substances;

· Specific environmental and ecosystem effects from accidental releases or incidents.

| Activity/Aspect | Environmental incidents and emergency preparedness |
| --- | --- |
| List of Associated Impacts | Pollution from chemical spillage Pollution from leaked oils Outbreak of fire Collapse of excavated holes Burst of a water pipe |
| Possible Causes | Lack of awareness and knowledge of incidents and control by staff Lack of control measures Lack of environmental emergency preparedness plan |
| Risks | Pollution of water courses Non-compliance and fines Increased rehabilitation costs Loss of work time Loss of property and assets |
| Mitigation | Compile an environmental emergency preparedness plan Identify environmental emergency cases Educate contract staff on the implementation of the plan Construction employees shall be adequately trained in terms of incidents and emergency situations. An emergency preparedness plan will include details of the organisation (manpower) and responsibilities, accountability and liability of personnel. The emergency preparedness plan shall include a list of key personnel. Details of emergency services (e.g. the fire department, spill cleanup services, etc.) shall be listed Incident recording, progress reporting, and remediation measures to be implemented shall be included. Information on hazardous materials, including the potential impact associated with each, and measures to be taken in the event of accidental release shall be listed In the event of a spillage during the construction phase, the responsibility for spill treatment will lie with the contractor and the contractor will be liable to arrange for competent assistance to clear the affected area The ECO will assess the situation in consultation with the contractor and act as required. In all cases, the immediate response will be to contain the spill. The exact treatment of polluted soil/water will be determined by the contractor in consultation with the ECO. Areas cleared of hazardous waste will be re-vegetated according to the ECO’s instructions. Should water downstream of the spill be polluted, and fauna and flora show signs of deterioration or death, specialist hydrological or ecological advice must be sought for appropriate treatment and remedial procedures to be followed. The requirement for such input will be agreed with the ECO. The costs of containment and rehabilitation will be for the contractor’s account, including the costs of specialist input Implement prevention measures such as firebreaks, placing impermeable mould under parked heavy vehicles or establish a concrete parking bay, establish earth wall bunds to contain runaway soil, install a separation tap to cut off the leaking pipe, have appropriate material to absorb oil and neutralise chemical spills When an incident occurs work at the area where the problem is taking place or on the site as whole should be stopped and attention should be applied on controlling the incident Environmental incidents such oil should be reported to the Project Coordinator/Manager |
| Responsible | Project manager, ECO, EEO |
| Timeframe | Daily |
| Targets | Zero incidents Implementation of emergency control measures Effective environmental emergency preparedness plan |
| KPI | Records of incidents and corrective actions Closure of incidents as completely controlled |
| Monitoring | Monthly and daily after occurrence of the incident |
| Environmental Standard Procedure | Emergency preparedness plan |
| Financial provision | Funds for containing environmental emergency on site and on neighbouring properties |

SEPARATION OF WASTE AND USE OF REGISTERED WASTE LANDFILL SITES

Objective: To ensure disposal at authorised sites

| Activity/Aspect | Waste management and use of registered waste site |
| --- | --- |
| List of Associated Impacts | Separation of waste for purpose of recycling Compliance with NEMA Waste Act Disposal of waste on monitored and well cared sites as per waste regulations |
| Possible Causes | Compliance with legislation |
| Risks | Fines and litigation as a result of illegal dumping Pollution of soil and water courses |
| Mitigation | Provision of separate bins for disposal of different waste Sufficient waste bins must be on the construction site to handle the amount of litter, wastes and rubbish debris and builders wastes generated on the site Waste bins must be securely covered at all times and emptied frequently to avoid rodents, insects or any other organisms accumulating on the site and becoming a health hazard to surrounding areas and construction site Waste material should be recycled where possible Proof of registration must be requested before disposal of waste Dispose only unrecyclable material at landfill sites Indiscriminate spillage of fuel or oil is not permitted Fuel and oil are to be disposed in allocated bins Fuel or oil are to be recycled or disposed at incineration places Scrap metal should be taken to Eskom depot for recycling All spoil material is to be located on designated areas within the demarcated footprint Rubbish is to be disposed in closed bins to prevent it being blown away |
| Responsible | Project supervisor |
| Timeframe | Daily |
| Targets | Zero percent waste on site Tonnage of recycled material |
| KPI | Records of recycled material Records of waste disposed at landfill site |
| Monitoring | Daily |
| Environmental Standard Procedure | Waste Management |
| Financial provision | Provision for transportation of waste to waste sites or recycling sites |

SERVICING AND RE-FUELLING OF CONSTRUCTION EQUIPMENT

Objective: To minimise and/or prevent pollution of natural environments by petrochemicals

| Activity/Aspect | Servicing and re-fuelling of construction equipment |
| --- | --- |
| List of Associated Impacts | Pollution of underlying soil Seepage into watercourses Killing of aquatic life Pollution of water used by livestock and animals Killing of grass where the leak occurred |
| Possible Causes | Leaks from unrepaired vehicles Lack of bund walls to contain major leaks or damaged containers Letting leaking vehicles stand without being sent for repair as soon as a leak is noticed Lack of placing containment equipment under serviced vehicles Lack of cleaning spills Placing of fuels and other petrochemicals in undesignated and non-lined ground |
| Risks | Contravention of law Fines and litigation Causing illness in livestock and humans |
| Mitigation | All maintenance and repair work will be carried at the construction site within an area designated for this purpose, equipped with necessary pollution containment measures. The ground under the servicing and refuelling areas must be protected against pollution caused by spills and / or tank overfills. These areas must be bunded or lined Oil or lubricant may be change only designated areas, except if there is a breakdown or emergency repair, and then any accidental spillages must be cleaned up or removed immediately In such cases drip trays must be made available to collect any oil or fluid coming from repairing vehicles No vehicles or equipment with leaks or causing spills should be permitted to operate at any of the construction sites. These vehicles must be sent immediately to the maintenance yard for repair. Fuels required during construction must be stored in designated areas within construction site. The fuel storage area should be located on a slab and be contained within a bund capable of containing the stored fuel |
| Responsible | Project supervisor and ECO |
| Timeframe | Daily |
| Targets | Zero spillage of fuel and oil Improved containment of oil and fuel in case of spillage Treatment of spillages |
| KPI | Records of spill incidents and applied corrective measures |
| Monitoring | Daily |
| Environmental Standard Procedure | None |
| Financial provision | Funds for rehabilitated polluted areas |

PART 3

7. COMPLETION OF WORK 							CHAPTER 7

Objective: To clear the site of all litter, rubble and dealing with pollution of soil and vegetation cover

7.1 	Rehabilitation and maintenance

| Activity/Aspect | Activities within construction site |
| --- | --- |
| List of Associated Impacts | Erosion and scouring Gullies due to extended erosion Littering Pollution Property damage |
| Possible Causes | Contractor lack of care band due diligence Poor understanding of environmental requirements and compliance Lack of rehabilitation plan No discussion and approval of rehabilitation plan Inadequate rehabilitation budget Poor post construction audit Poor stabilisation of disturbed areas Poor application of waste management plan No non-compliance issued Poor closure of identified issues Lack of follow-up on incident and environmental management |
| Risks | Loss of topsoil Littering and pollution Damage to Eskom reputation Non-compliance to applicable legislation Litigation |
| Mitigation | After completing construction the contractor shall clear and remove from the site all construction waste such as empty containers, surplus materials, temporary foundations, temporary plumbing and other fixtures, rubbish and temporary work of every kind Areas thus cleared shall be graded and scarified and rehabilitated according to rehabilitation specification Rehabilitation plan must be approved by the ECO Rehabilitation must be done according to the approved rehabilitation plan All rehabilitation to achieve approved status by handover time All disturbed areas shall be repaired, revegetated and rehabilitated to the satisfaction of the ECO The Contractor shall use only grasses and vegetation occurring naturally in the area for this purpose Only indigenous species endemic to the area shall be used The Contractor shall maintain all vegetative work provided as part of, or resulting from his activities until the end of the contract period or until vegetation is properly established, whichever period is the longer Particular attention must be paid to the control of erosion of new and disturbed areas, spoil heaps The ECO shall monitor the revegetation programme submitted by the Contractor so as to determine the adequate recovery of all disturbed areas All damaged property must be repaired and compensated where applicable Completed and approved site exit plan Alien species must be removed from construction site All spoil must be removed from site and disposed accordingly Confirmation of use of registered landfill site must be available in the project file All temporary structures and facilities shall be properly and safely decommissioned and removed from site once all construction activity associated with such facilities has ceased Closure, decommissioning and rehabilitation shall extend to removing any residual pollution or sources of pollution |
| Responsible | Construction supervisor, Construction manager, Project Engineer and ECO |
| Timeframe | Post construction |
| Targets | No litter Incident and environmental closure Approved site exit plan No waste No damage to private property Approved rehabilitated areas |
| KPI | Signed site exist plan Approved rehabilitation status No alien species Documented incident register Documented incident management plan |
| Monitoring | Monthly |
| Environmental Standard Procedure | Waste management Eskom Entering private properties procedures |
| Financial provision |  |

PART 4

8. 	OPERATION AND MAINTENANCE 					CHAPTER 8

8.1 	Ground maintenance and safety

Objective: To prevent erosion, spread of fire rubbish lying around becoming a fire hazard

| Activity/Aspect | Ground maintenance and effective safety |
| --- | --- |
| List of Associated Impacts | Potential erosion Eroded soil and silt landing on HV yard affecting quality of supply Waste lying around Tall grass a safety hazard Silted drains leading to improper channelling of run-off Poor grass cover around the tower bases Weed invasion |
| Possible Causes | Poor ground cover Poor ground maintenance |
| Risks | Loss of topsoil Loss of supply Accidents Spread of fire Costs involved in importing soil to compensate for lost topsoil |
| Mitigation | Planted areas need to be monitored for good cover Grass is to be cut short to prevent spread of fire and hiding of snakes Weeds are to be removed during cutting of grass All waste is to be removed along the servitude long the entire powerline Maintenance of suitable firebelts All areas where safety has been compromise need to be fixed Access road is to be monitored for good status and proper compaction Poor road condition must be corrected Silted drains are to be excavated and sloped accordingly Dissipaters at the end of drains must be maintained in good conditions to prevent scouring Local Eskom office must report on any evidence of animal interaction and fatality Ablution facilities at the control room must be checked to be in good condition All safety signs along the powerline must be checked to be in good order and replaced tarnished signs All complaints from neighbouring residents must be recorded and attended to |
| Responsible | Eskom area manager and supervisor, EEO |
| Timeframe | Monthly or according to inspection schedule |
| Targets | Zero waste along the powerline servitude All grass cover is to be cut All areas breached of safety are to be fixed with immediate effect |
| KPI | Records showing grassing schedule Lack of waste within and immediately along the powerline |
| Monitoring | Monthly |
| Environmental Standard Procedure | Ground maintenance |
| Financial provision | Funds needed for grassing in areas showing poor growth Ground maintenance costs |

PART 9

9.	MONITORING OF EMP IMPLEMENTATION 				CHAPTER 9

The correct and successful implementation of impact mitigation measures in order to reduce adverse impacts on environmental conditions needs to be ensured by a proper monitoring programme.

Monitoring of the general implementation of/adherence to the EMP, shall be the responsibility of the ECO.

Reporting on adherence/compliance to stipulations as communicated to contractors, shall take place during scheduled site meetings.

9.1 	Report on monitoring

ECO undertakes a monthly visit to monitor implementation of the EMP and report finding in a comprehensive report. The report can assume any format including the EMP format to keep consistency. The ECO is to report on findings to the project manager and project engineer at the site meeting.

Appendix A

Audit Schedule

| Audit level | Project activity | Audit type | Frequency |
| --- | --- | --- | --- |
| Project management | Policy availability | Project management | Twice annually |
|  | EMP implementation |  |  |
|  | Waste management plan |  |  |
|  | Audit plan |  |  |
| Site management | Policy application | Compliance | Twice annually |
|  | Permits |  |  |
|  | EMP |  |  |
|  | Audit reports |  |  |
|  | EMP compliance |  |  |
|  | Staff environmental awareness and training |  |  |
|  | Training of sub-contractors |  |  |
|  | Training records |  |  |
| EMP compliance site general | Waste management | Compliance | Monthly |
|  | Site plan |  |  |
|  | Site storage plan |  |  |
|  | Site drainage plan |  |  |
|  | Site storage |  |  |
|  | Site demarcation and signage |  |  |
|  | Chemical ablution |  |  |
|  | Potable water |  |  |
|  | Waste management |  |  |
|  | Use of registered landfill site |  |  |
|  | Sensitive areas |  |  |
|  | Access |  |  |
|  | Vehicle movement |  |  |
|  | Incident management |  |  |
|  | Emergency preparedness |  |  |
|  | Control of alien vegetation |  |  |
| Work area | Demarcation of work area | Compliance | Monthly |
|  | Dust management |  |  |
|  | Noise management |  |  |
|  | Spoil storage |  |  |
|  | Alien vegetation control |  |  |
|  | Potable water |  |  |
|  | Demarcation of smoking area |  |  |
| Rehabilitation compliance | Approved rehabilitation programme | Compliance | Monthly |
|  | Rehabilitation progress |  |  |

# Text boxes

Ludloko Developments (LDK) CC
 CK 2000/024018/23

Vat Reg. No. 4620188781
Agricultural Development & Sustainable Environmental Management
P.O. Box 22964
Southgate, Pietermaritzburg, 3200
Fax: 086 570 8493 Cell: 084 565 0531

E-mail: dudungidi@vodamailco.za